## Slide 1
EV Systems Internship
Second Review — May 7, 2026 Upgraded Projects & Progress Review 2

## Slide 2
Review Period: April 16 – May 7
Duration & Activity
• Intensive development phase focused on project upgrades
• Transitioned from basic prototypes to production-grade systems
• Both projects renamed and evolved into full-fledged applications
• Code testing, debugging, and integration completed
Key Milestones
• Project 1 renamed: EV Battery Telemetry System (enhanced from SOC Indicator)
• Project 2 renamed: Cell Balancing & SOH Estimation System (enhanced from EV Dashboard)
• Data logging, CSV export, and visualization features added
• Comprehensive testing on multiple battery chemistry profiles

## Slide 3
Project 1: EV Battery Telemetry System
System Architecture
• Real-time battery monitoring with multi-chemistry support (NMC, LFP, NCA, LMO)
• Advanced SOC calculation with polynomial OCV curves
• State of Health (SOH) estimation based on capacity fade models
• Voltage, current, temperature, and aging monitoring
Core Features
• Live arc gauges showing battery status with real-time needle positioning
• Color-coded status badges (CRITICAL, LOW, GOOD, OPTIMAL)
• Automatic CSV data logging with timestamp and parameter history
• Database of 4 battery chemistry profiles with physics-based parameters

## Slide 4
Project 1: Telemetry System Features (Continued)
Data Analysis & Visualization
• SOC history graph – displays battery discharge curve over time
• Capacity fade tracking – visual representation of aging progression
• Thevenin equivalent circuit modeling for accurate terminal voltage
• Multi-parameter alerts for voltage, temperature, and resistance anomalies
Battery Chemistry Intelligence
• NMC (Li-ion NMC): 40–54V range, 200–300 Wh/kg, 1,200–2,800 cycles
• LFP (Lithium Iron Phosphate): 42–58.4V range, 120–200 Wh/kg, 2,000–6,000 cycles
• NCA (Nickel Cobalt Aluminum): 40–54.6V range, 250–320 Wh/kg, 500–1,500 cycles
• LMO (Lithium Manganese Oxide): 40–54V range, practical automotive use

## Slide 5
Project 2: Cell Balancing & SOH Estimation System
System Purpose
• Simulates cell balancing algorithms for multi-cell battery packs
• Estimates battery State of Health (SOH) based on capacity fade and resistance aging
• Models the physical behavior of active balancing in real battery management systems
• Predicts remaining useful life (RUL) using polynomial regression
Advanced Modeling
• Thevenin equivalent circuit for each battery cell with RC dynamics
• Coulomb counting for accurate SOC tracking during charge/discharge cycles
• Capacity fade model: SOH = 100% × (1 - k × cycle^β)
• Resistance aging model with temperature-dependent Arrhenius factors

## Slide 6
Project 2: Cell Balancing Algorithm
Active Balancing Mechanism
• Monitors individual cell voltages in 4S (series) configuration
• Triggers balancing resistor when voltage difference exceeds 20mV threshold
• Dissipates excess energy from higher-voltage cells (22Ω balancing resistor)
• Continuous monitoring during simulation to keep cells within ±10mV
SOH Estimation Methods
• Capacity fade tracking: degradation follows k×cycle^β power law
• Resistance-based SOH: monitors internal resistance increase over cycles
• Multi-parameter assessment combining capacity and resistance indicators
• End-of-life (EOL) threshold set at 80% SOH per industry standards

## Slide 7
Project 2: Visualization & Analysis
Real-Time Dashboards
• Individual cell voltage monitoring with live updates every 10 seconds
• Pack-level SOC, SOH, and internal temperature displays
• Balancing current visualization showing active energy redistribution
• Multi-cycle simulation (up to 500 cycles) with time compression
Data Export & Prediction
• CSV export of all cell voltages, currents, temperatures per cycle
• Cumulative degradation tracking and trend analysis
• ML-based RUL prediction using polynomial regression on SOH history
• Arrhenius temperature acceleration factor for realistic aging rates

## Slide 8
Technical Architecture
Project 1: Telemetry
• Python 3 + Tkinter GUI
• Matplotlib for real-time graphing
• CSV logging for data persistence
• OCV polynomial fitting
• Thevenin circuit simulation
• 4 chemistry database profiles
Project 2: Cell Balancing
• NumPy arrays for cell state tracking
• Matplotlib gridspec for multi-panel UI
• CSV export for cycle history
• Threading for real-time simulation
• Advanced battery cell modeling
• RUL prediction with scipy

## Slide 9
Testing & Validation (Apr 16 - May 7)
Project 1 Testing
• 10+ manual test cases across all battery chemistries
• Edge case validation: boundary voltages at 20% and 50% SOC thresholds
• CSV logging verified with timestamp and calculation accuracy
• Graph rendering tested for discharge curve smoothness
Project 2 Testing
• Multi-cycle simulation tested for 100, 250, and 500 complete cycles
• Cell balancing verified: voltage deviation stayed within ±15mV
• SOH estimation validated against theoretical capacity fade curves
• RUL prediction accuracy checked with historical cycle data

## Slide 10
Challenges Faced & Solutions
Technical Challenges
• Thevenin model convergence at extreme SOC values
• Real-time graph rendering lag with 500-cycle data
• CSV file locking during concurrent read/write operations
• Temperature-dependent resistance calculation complexity
Solutions Implemented
• Added SOC clipping (0.01–0.99) and exponential smoothing
• Optimized matplotlib update frequency to 100ms refresh rate
• Implemented queue-based file I/O with thread-safe locks
• Integrated Arrhenius equation with lookup tables for efficiency

## Slide 11
Current Status & Completion
What Is Complete
• Project 1 (Telemetry): All core features + data logging + visualization ✓
• Project 2 (Cell Balancing): All physics + balancing + SOH estimation ✓
• Comprehensive CSV export for both projects ✓
• User-friendly Tkinter GUI with real-time updates ✓
• Project reports finalized and submitted ✓
Known Issues & Fixes in Progress
• Minor: Occasional graph jitter at 500 cycle boundary (targeted fix for final review)
• Minor: CSV headers need Unicode normalization for Excel compatibility
• Planned: Additional noise filtering for noisy sensor data

## Slide 12
Final Review Preparation (May 8 – 14)
Final Presentation Scheduled
• Second Review: May 8, 2026 – Live demonstration of both projects
• Final Presentation: May 14, 2026 – Complete project showcase
• Code testing & bug fixes on approved execution platform
• Documentation finalization and student feedback incorporation
Enhancements for Final Review
• Additional test case documentation showing real-world battery behavior
• Performance benchmarks (execution time, memory usage)
• Detailed technical report with circuit diagrams and algorithms
• Video walkthrough of both projects for reference

## Slide 13
Key Learnings from This Phase
Battery Management Science
• Deep understanding of SOC estimation algorithms used in production BMS
• How capacity fade follows predictable mathematical models (power law)
• Importance of cell balancing in extending pack lifetime and safety
• Real-world temperature effects on battery aging and performance
Software Engineering
• Building robust multi-threaded applications with real-time constraints
• Effective data visualization for complex scientific simulations
• Importance of comprehensive testing before production deployment
• How physics-based modeling improves software reliability and accuracy

## Slide 14
Thank You
Second Review — May 7, 2026 Department of Electrical Engineering