## Slide 1
EV Systems Internship
Intermediate Review — April 2026
Domain: Embedded Systems | EV Battery Monitoring
Department of Electrical & Electronics Engineering | 2025 – 2026
Review 1
K Vamsi Krishna | 4UB22EE020 | 8th Semester
University B D T College of Engineering
(A Constituent college of Visvesvaraya Technological University, Belagavi)
Davanagere - 577004

## Slide 2
Internship Overview
Organization
EV Academy
Internship Program
Electric Vehicle Systems
Duration
February 2026
to May 2026
(Ongoing)
Domain
Embedded Systems
EV Battery Monitoring
Software Simulation
This internship combined structured online learning sessions with hands-on software project development in EV systems.

## Slide 3
Phase 1 — Learning & Training (February 2026)
What We Did
What We Did
Attended daily sessions with EV Academy
Sessions led by industry mentors with hands-on demos
Covered both hardware concepts and software tools
Included practical simulations using Arduino and MATLAB
Topics Covered
Battery Technology & Chemistry
Battery Management Systems (BMS)
Series & Parallel Pack Design
Motor Control & BLDC Motors
Power Electronics & Inverters
Charger Selection & CC-CV Method
Embedded Systems & Arduino
PWM, ADC & Sensor Integration

## Slide 4
Phase 2 — Team Formation & Project Selection (March 1–16)
1
Team Formation
Formed project group
Team Tactical Thinkers
Defined team roles clearly.
2
Topic Research
Reviewed project list from
officially provided documents
Analyzed feasibility of options.
3
Ideation
Brainstormed solution approaches
Decided on EV Battery Monitoring
as our core focus area.
4
Project Finalization
Selected Battery SOC Indicator
and EV Dashboard as projects
Submitted official project title
Project titles were drawn from the officially provided EV project list documents given during internship.

## Slide 5
Project 1 — Battery State of Charge (SOC) Indicator
What It Does
User enters battery voltage as input
Program calculates SOC using linear mapping formula
Result shown as percentage with colored progress bar
Color coded status: Green (Safe), Yellow (Low), Red (Critical)
Advisory message guides user on what action to take
Invalid inputs handled with clear error messages
Built entirely using Python and Tkinter only
SOC Formula
SOC (%) = [ (V - V_min) / (V_max - V_min) ] x 100
V_min = 40.0 V (0% SOC) V_max = 54.0 V (100% SOC)
Status Thresholds
SAFE
SOC above 50%
LOW
SOC between 20% and 50%
CRITICAL
SOC below 20%

## Slide 6
Project 2 — EV Dashboard GUI Application
Arc Gauge Display
Three real-time arc gauges for Speed, Battery, and Temperature. Needle position calculated using trigonometry (cos & sin).
Auto Simulation Mode
Simulates live driving behavior. Speed drifts randomly, battery depletes gradually, temperature rises with speed.
Multi-Parameter Alerts
Monitors all three parameters simultaneously. Battery below 20%, temperature above 50°C, and speed above 100 km/h trigger alerts.
Information Panel
Shows estimated range, power draw, efficiency rating, and current drive mode calculated from live values.

## Slide 7
Testing & Results
Battery SOC Indicator — Test Cases
Input | SOC | Status | Result
54.0 V | 100.0% | SAFE | PASS
47.0 V | 50.0% | SAFE | PASS
44.8 V | 34.3% | LOW | PASS
42.0 V | 14.3% | CRITICAL | PASS
60.0 V | 100% (capped) | SAFE | PASS
"abc" | — | Error shown | PASS
-5.0 V | — | Error shown | PASS
Input SOC Status Result
EV Dashboard — Key Observations
10 manual test combinations all passed correctly
Arc gauges filled and needle positioned accurately for all values
Status badges changed color correctly at all threshold boundaries
All three alerts appeared simultaneously when test case 8 was run
Auto simulation ran for 2 minutes with no freezing or lag
Battery hitting zero correctly forced speed to zero
Temperature cooled down after speed dropped to zero
Reset button correctly restored all default values
Application ran without errors across all test sessions

## Slide 8
Current Status & Challenges Faced
What Is Complete
Battery SOC Indicator core logic complete
EV Dashboard with all three gauges working
Auto simulation mode tested and verified
Alert system working for all three conditions
10 test cases documented and all passed
Both project reports drafted
Internship diary maintained from February
Challenges We Faced
Arc Gauge Math
Understanding how Tkinter's coordinate system maps to angles required careful study of trigonometry and manual diagram tracing before it clicked.
Simulation Bug Fix
Temperature kept rising even after battery hit zero. Fixed by adding a specific check so temperature cools down when speed drops to zero.
Edge Case at 47V
Voltage of exactly 47V gives exactly 50% SOC which sits right on the threshold. Documented clearly to avoid confusion during evaluation.
Input Validation
Ensuring the program does not crash on text inputs or negative values required proper try-except handling around the calculation function.

## Slide 9
Planned Upgrades & Future Scope
Project 1 | Data Logging to CSV
Every SOC calculation gets saved to a CSV file automatically with timestamp, voltage, and SOC value. Creates a historical record of battery readings.
Project 1 | SOC History Graph
A second screen that reads the logged CSV and plots a line graph showing how SOC changed over multiple readings. Visualizes battery discharge pattern.
Project 2 | Trip Summary Popup
When simulation stops a popup shows total estimated distance covered, average speed, battery consumed, and peak temperature recorded during the trip.
Project 2 | Temperature Trend Graph
A small live graph drawn below the dashboard that shows temperature change over the last 20 simulation ticks using Tkinter Canvas lines.
These upgrades will make both simulations closer to real-world EV monitoring systems and will be demonstrated in Review 2.

## Slide 10
Key Learnings from This Internship
1
How battery SOC is calculated in real BMS systems and why threshold values like 20% and 50% are chosen based on lithium-ion cell safety.
2
How series and parallel cell connections affect voltage and capacity, and how to design a battery pack for a specific voltage requirement.
3
How BLDC motors use Hall sensors and MOSFET switching to maintain rotation and how regenerative braking works in reverse.
4
How arc gauges in real EV dashboards are implemented using trigonometry and how color coding communicates system status instantly.
5
How input validation and edge case testing are as important as building the main feature when developing reliable software systems.
6
How to structure a software project from problem statement through design, implementation, testing, and documentation in report form.

## Slide 11
Thank You
Intermediate Review — April 2026
Department of Electrical Engineering | 2025 – 2026